|  |  | Spec. No. | HP-L217 |
| --- | --- | --- | --- |
|  | 870nm INFRARED LED | Part | LED |

| CUSTOMER : |  |
| --- | --- |
| DEVICE NAME : |  |
| MODEL NO. : |  |
| ISSUED DATE : |  |

[ CUSTOMER APPROVAL ]

| APPROVAL NO. |  |
| --- | --- |
| APPROVAL DATE |  |
| APPROVAL | INSPECTER | CHECK | APPROVAL | COMMENT |

[ SUPPLIER ]

| ISSUED DEPT. | ISSUE | REVIEW | REVIEW | APPR’D |
| --- | --- | --- | --- | --- |

|  |  | Spec. No. | HP-L217 |
| --- | --- | --- | --- |
|  | 870nm INFRARED LED | Part | LED |

- CONTENTS -

1. FEATURES

2. OUTLINE DIMENSIONS

3. SPECIFICATIONS

4. COMPOSITION OF DEVICE

5. ELECTRO-OPTICAL CHARACTERISTICS CURVES

6. RELIABILITY

7. TAPING

8. PACKING

9. CUATIONS

|  |  | Spec. No. | HP-L217 |
| --- | --- | --- | --- |
|  | 870nm INFRARED LED | Part | LED |

1. FEATURES

▪ SMD Top View type

▪ 870nm Infrared Emitting GaN

▪ High Radiant Intensity

▪ Viewing angle : Lambertian emitter(120˚)

▪ Package size : 1.6 × 0.8 × 0.4

▪ Reliability test completion

▪ Suitable for all SMT assembly methods

2. OUTLINE DIMENSIONS

|  |  | Spec. No. | HP-L217 |
| --- | --- | --- | --- |
|  | 870nm INFRARED LED | Part | LED |

3. SPECIFICATIONS

▣ Absolute Maximum Rating

(Ta=25℃)

| Parameter | Symbol | Value | Unit |
| --- | --- | --- | --- |
| Power Dissipation | PD | 120 | ㎽ |
| Peak Forward Current ▶ 1 | IFP | 0.5 | A |
| Reverse Voltage | VR | 5 | V |
| Forward Current | IF | 80 | ㎃ |
| Operating Temperature | Topr | -35 to + 85 | ℃ |
| Storage Temperature | Tstg | -40 to + 85 | ℃ |
| Soldering temperature | Tsol | Reflow soldering : 240℃, 10 sec Hand Soldering : 300℃, 3 sec |

▶ 1 : Duty Ratio ≤ 1/100, Pulse Width ≤ 0.01 msec.

▣ Electro-Optical Characteristics

(Ta=25℃)

| Parameter | Symbol | Condition | Min | Typ | Max | Unit |
| --- | --- | --- | --- | --- | --- | --- |
| Forward Voltage | VF | IF=20㎃ | - | 1.4 |  | V |
| Reverse Current | IR | VR=5V | - | - | 10 | ㎂ |
| Radiant Intensity | Po | IF=20㎃ | - | 5 | - | mW |
| Viewing Angle ▶ 3 | 2θ1/2 | IF=20㎃ | - | ±60 | - | deg. |
| Peak Wavelength | λP | IF=20㎃ | - | 870 | - | nm |

▶ 3 : θ1/2 is the off-axis angle at which the luminous intensity is half the peak intensity.

※ Measurement Uncertainty : ± 10%

|  |  | Spec. No. | HP-L217 |
| --- | --- | --- | --- |
|  | 870nm INFRARED LED | Part | LED |

4. COMPOSITION OF DEVICE

A. MATERIALS OF PACKAGE

| Number | Item | Material |
| --- | --- | --- |
| 1 | Die adhesive | Ag Epoxy |
| 2 | LED Chip | AlGaAs |
| 3 | Au Wire | 1.0mil |
| 4 | Mold epoxy | Epoxy Resin |
| 5 | Electrodes | Au Plating Cu Alloy |

B. DIAGRAM OF COMPOSITION

| ` |  | Spec. No. | HP-L217 |
| --- | --- | --- | --- |
|  | 870nm INFRARED LED | Part | LED |

5. ELECTRO-OPTICAL CHARACTERISTICS CURVES

|  |  | Spec. No. | HP-L217 |
| --- | --- | --- | --- |
|  | 870nm INFRARED LED | Part | LED |

5. ELECTRO-OPTICAL CHARACTERISTICS CURVES

|  |  | Spec. No. | HP-L217 |
| --- | --- | --- | --- |
|  | 870nm INFRARED LED | Part | LED |

6. RELIABILITY

A. TEST ITEMS AND RESULTS

| Test Item | Standard test method | Test Conditions | Note | Number of Damaged |
| --- | --- | --- | --- | --- |
| Resistance to Soldering Heat (Reflow Soldering) | JEITA ED-4701 300 301 | Tsol=240℃, 10sec. (Pre treatment 30℃, 70%, 168hrs.) | 2 times | 0/50 |
| Solderability (Reflow Soldering) | JEITA ED-4701 100 105 | Tsol=215±5℃, 3sec. | 1 time over 95% | 0/50 |
| Heat Shock | JEITA ED-4701 100 105 | 0℃ ~ 100℃ 5sec. 15sec. | 20 cycles | 0/50 |
| Temperature Cycle | JEITA ED-4701 100 105 | -40℃ ~ 25℃ ~ 100℃ ~ 25℃ 15min. 5min. 15min. 5min. | 100 cycles | 0/50 |
| High Humidity Heat Cycle | JEITA ED-4701 200 203 | 30℃ ~ 65℃ ~ -10℃ 90%RH 24hrs./1cycle | 10 cycles | 0/50 |
| High Temperature Storage | JEITA ED-4701 200 203 | Ta=100℃ | 1000 hrs. | 0/50 |
| Humidity Heat Load | JEITA ED-4701 100 103 | Ta=60℃, RH=90% | 1000 hrs. | 0/50 |
| Low Temperature Storage | JEITA ED-4701 200 202 | Ta=-40℃ | 1000 hrs. | 0/50 |
| Life Test Condition 1 |  | Ta=25℃, IF=20mA | 1000 hrs. | 0/50 |
| High Temperature Life Test |  | Ta=85℃, IF=5mA | 1000 hrs. | 0/50 |
| High Humidity Heat Life Test |  | 60℃, RH=90%, IF=15mA | 500 hrs. | 0/50 |
| Low Temperature Life Test |  | Ta=-30℃, IF=20mA | 1000 hrs. | 0/50 |

B. CRITERIA FOR JUDGING THE DAMAGE

| Item | Symbol | Test Conditions | Criteria for Judgement |
| --- | --- | --- | --- |
|  |  |  | Min. | Max. |
| Forward Voltage Reverse Current Luminous Intensity | VF IR IV | IF=20mA VR=5V IF=20mA | - - L.S.L.**) × 0.7 | U.S.L.*) × 1.1 U.S.L.*) × 2.0 - |

*) U.S.L. : Upper Standard Level        **) L.S.L. : Lower Standard Level

|  |  | Spec. No. | HP-L217 |
| --- | --- | --- | --- |
|  | 870nm INFRARED LED | Part | LED |

7. TAPING

| ` |  | Spec. No. | HP-L217 |
| --- | --- | --- | --- |
|  | 870nm INFRARED LED | Part | LED |

8. PACKING

| ` |  | Spec. No. | HP-L217 |
| --- | --- | --- | --- |
|  | 870nm INFRARED LED | Part | LED |

9. CUATIONS

(1) Moisture Proof Package

  - When moisture is absorbed into the LEDs it may vaporize and expand during soldering. There is a possibility that this can cause the exfoliation of the contacts and the damage the optical characteristics of the LEDs. For this reason, the moisture proof package is used to keep moisture to a minimum in the package.

  - After opening the package, the LEDs should be kept at 30℃, 40~70%RH.

The LEDs should be soldered within 168 hours(7days) after opening the package.

- When storing the LEDs after opening the package, use a sealable away from package with a moisture absorbent material(Silica gel) inside.

- If the blue color of the desiccant indicator has faded after storing, a baking treatment should be performed as follows : 65 ± 5℃ for more than 24 hours.

(2) Soldering Conditions

- The LEDs can be soldered in place using the reflow soldering method.

- The recommended soldering conditions are as follows:

| Reflow Soldering | Hand Soldering |
| --- | --- |
|  | Lead Solder | Lead-free Solder |  |  |
| Pre-heat | 120~150℃ | 180~200℃ | Temperature | 350℃ Max |
| Pre-heat time | 120sec Max | 120sec Max | Soldering time | 3sec Max |
| Peak temperature | 240℃ Max | 260℃ Max |  | (one time only) |
| Soldering time | 10sec Max | 10sec Max |  |  |
| Condition | refer to | refer to |  |  |
|  | Temperature | Temperature |  |  |
|  | profile ① | profile ② |  |  |
| * After reflow soldering rapid cooling should be avoided. |  |  |

|  |  | Spec. No. | HP-L217 |
| --- | --- | --- | --- |
|  | 870nm INFRARED LED | Part | LED |

- Temperature-Profile

- Recommended Soldering

- Modifications should not be done after the LEDs have been soldered.

If modifications cannot be avoided, a double-head soldering iron should be used after checking whether the characteristics of the LEDs will not be damaged by modification after soldering.

- Reflow soldering, do not apply force to the package during heating.

- After soldering, do not warp the circuit board.

(3) Heat Generation

- Heat generation must be taken into design consideration when using the LEDs.

The coefficient of temperature increase per input electric power is about 0.62℃/mW at the LED’s active layer. This coefficient will be affected by the heat resistance of the circuit board and by dense mounting of the LEDs. At the same time, precautions must be taken into the design of circuitry to avoid intense heat generation. Proper designs which allow radiation of heat, etc. may be needed.

|  |  | Spec. No. | HP-L217 |
| --- | --- | --- | --- |
|  | 870nm INFRARED LED | Part | LED |

(4) Static Electricity

- Static Electricity and surge damages the LEDs. It is recommended to use a wrist band or anti-electrostatic glove when handling the LEDs.

- All devices, equipment and machinery must be properly grounded.

- When inspecting own final products on which LEDs were mounted, it is recommended to check also whether the mounted LEDs are damaged by static electricity or not.

- Damaged LEDs will show some unusual characteristics such as leak current remarkably increases, starting forward voltage becomes lower, or the LEDs get unlighted at the low current.

(5) Cleaning

- Use Isopropyl Alcohol as a solvent for cleaning the LEDs. Using other solvents may dissolve the LED package and the epoxy. Caution is needed.

Ultrasonic cleaning of the LEDs should not be done.

(6) Others

- The electrode sections are plated with silver. Those will become discolored by contact with corroded gas etc. Precautions must be taken to maintain a clean storing atmosphere.

- These LEDs described in this brochure are intended to be used for ordinary electronic equipment. Consult HANSE’s sales staff in advance for information on the applications in which exceptional quality and reliability are required, particularly when the failure or malfunction of the LEDs may directly jeopardize life or health (such as airplanes, aerospace, automobiles, life support systems and safety devices).

- User shall not reverse engineer by disassembling or analysis of the LEDs without having the prior written consent of HANSE. When defective LEDs are found, User shall inform to HANSE directly before disassembling or analysis.

- The appearance and specifications of the product may be modified for improvement without notice.

# Text boxes

Electronics corp.

HANSE SENSOR SERIES

HC-870T1608B

2017Rev : 1.0

SPECIFICATION

HANSE ELECTRONICS CORP.

TEL : 82-31-206-2851   FAX : 82-31-206-2850

http://www.e-hanse.com

HESP-KA-034

1/13

2017Rev : 1.0

HC-870T1608B

Electronics corp.

HANSE SENSOR SERIES

HANSE ELECTRONICS CORP.

TEL : 82-31-206-2851   FAX : 82-31-206-2850

http://www.e-hanse.com

HESP-KA-034

2/13

2017Rev : 1.0

HC-870T1608B

Electronics corp.

HANSE SENSOR SERIES

HC-870T1608B

(Unit : mm)

2-□0.5

5.0

HANSE ELECTRONICS CORP.

TEL : 82-31-206-2851   FAX : 82-31-206-2850

http://www.e-hanse.com

HESP-KA-034

3/13

2017Rev : 1.0

HC-870T1608B

Electronics corp.

HANSE SENSOR SERIES

HANSE ELECTRONICS CORP.

TEL : 82-31-206-2851   FAX : 82-31-206-2850

http://www.e-hanse.com

HESP-KA-034

4/13

2017Rev : 1.0

HC-870T1608B

Electronics corp.

HANSE SENSOR SERIES

HANSE ELECTRONICS CORP.

TEL : 82-31-206-2851   FAX : 82-31-206-2850

http://www.e-hanse.com

HESP-KA-034

5/13

2017Rev : 1.0

HC-870T1608B

Electronics corp.

HANSE SENSOR SERIES

■ Forward Voltage Vs. Forward Current

■ Forward Current Vs. Relative Luminosity

Function :

Function :

■ Relative Luminosity Vs. Ambient Ta(℃)

■ Forward Current Derating Curve

Function :

Function :

HANSE ELECTRONICS CORP.

TEL : 82-31-206-2851   FAX : 82-31-206-2850

http://www.e-hanse.com

HESP-KA-034

6/13

2017Rev : 1.0

HC-870T1608B

Electronics corp.

HANSE SENSOR SERIES

■ Radiation Characteristics

■ Relative Radiant intensity vs. Wavelength

HANSE ELECTRONICS CORP.

TEL : 82-31-206-2851   FAX : 82-31-206-2850

http://www.e-hanse.com

HESP-KA-034

7/13

2017Rev : 1.0

HC-870T1608B

Electronics corp.

HANSE SENSOR SERIES

HANSE ELECTRONICS CORP.

TEL : 82-31-206-2851   FAX : 82-31-206-2850

http://www.e-hanse.com

HESP-KA-034

8/13

2017Rev : 1.0

HC-870T1608B

Electronics corp.

HANSE SENSOR SERIES

A. Dimension of Tape ( Material : PS Carbon, 10E5Ω )

(Unit : mm)

0.85±0.05

B. Dimension of Wheel ( Material : PS Conductive, 10E9~12Ω )

(Unit : mm)

Loading quantity

per reel

: 4,000pcs

HANSE ELECTRONICS CORP.

TEL : 82-31-206-2851   FAX : 82-31-206-2850

http://www.e-hanse.com

HESP-KA-034

9/13

2017Rev : 1.0

HC-870T1608B

Electronics corp.

HANSE SENSOR SERIES

A. Packing diagram

2-□0.5

5.0

B. Precaution

A. The label on the minimum packing unit shows : Part Number, Lot Number, Ranking, Quantity

In order to protect the LEDs from mechanical shock, we pack them in cardboard boxes for

transportation.

B. The LEDs may be damaged if the boxes are dropped or receive a strong impact against them,

so precautions must be taken to prevent any damage.

C. The boxes are not water resistant and therefore must be kept away from water and moisture.

When the LEDs are transported, we recommend that you use the same packing method as

HANSE Electronics

HANSE ELECTRONICS CORP.

TEL : 82-31-206-2851   FAX : 82-31-206-2850

http://www.e-hanse.com

HESP-KA-034

10/13

2017Rev : 1.0

HC-870T1608B

Electronics corp.

HANSE SENSOR SERIES

HANSE ELECTRONICS CORP.

TEL : 82-31-206-2851   FAX : 82-31-206-2850

http://www.e-hanse.com

HESP-KA-034

11/13

2017Rev : 1.0

HC-870T1608B

Electronics corp.

HANSE SENSOR SERIES

(Unit : mm)

HANSE ELECTRONICS CORP.

TEL : 82-31-206-2851   FAX : 82-31-206-2850

http://www.e-hanse.com

HESP-KA-034

12/13

2017Rev : 1.0

HC-870T1608B

Electronics corp.

HANSE SENSOR SERIES

HANSE ELECTRONICS CORP.

TEL : 82-31-206-2851   FAX : 82-31-206-2850

http://www.e-hanse.com

HESP-KA-034

13/13