|  |  | Spec. No. | HP-L322 |
| --- | --- | --- | --- |
|  | SINGLE PHOTO DIODE:750~1100nm | Part | SENSOR |

| CUSTOMER : |  |
| --- | --- |
| DEVICE NAME : |  |
| MODEL NO. : |  |
| ISSUED DATE : |  |

[ CUSTOMER APPROVAL ]

| APPROVAL NO. |  |
| --- | --- |
| APPROVAL DATE |  |
| APPROVAL | INSPECTER | CHECK | APPROVAL | COMMENT |

[ SUPPLIER ]

| ISSUED DEPT. | ISSUE | REVIEW | REVIEW | APPR’D |
| --- | --- | --- | --- | --- |

|  |  | Spec. No. | HP-L322 |
| --- | --- | --- | --- |
|  | SINGLE PHOTO DIODE:750~1100nm | Part | SENSOR |

- CONTENTS -

1. FEATURES

2. APPLICATION

3. OUTLINE DIMENSIONS

4. SPECIFICATIONS

5. ELECTRO-OPTICAL CHARACTERISTICS CURVES

6. SELECTION GUIDE : CLASSIFICATION BY NAME

|  |  | Spec. No. | HP-L322 |
| --- | --- | --- | --- |
|  | SINGLE PHOTO DIODE:750~1100nm | Part | SENSOR |

1. FEATURES

▪ Photo diode

▪ High Speed, High sensitive Chip used

▪ PCB with DAYLIGHT FILTER

2. APPLICATION

▪ 940nm source suitable perfectably.

▪ Wide angle response

▪ High speed response

▪ Optical module

3. OUTLINE DIMENSIONS

|  |  | Spec. No. | HP-L322 |
| --- | --- | --- | --- |
|  | SINGLE PHOTO DIODE:750~1100nm | Part | SENSOR |

4. SPECIFICATIONS

▣ Absolute Maximum Ratings

(Ta=25℃)

| Parameter | Symbol | Value | Unit |
| --- | --- | --- | --- |
| Reverse Breakdown Voltage | BVR | 30 | V |
| Power Dissipation | PD | 150 | mW |
| Operating Temperature Range | TOPR | -10 ~ 80 | ℃ |
| Storage Temperature Range | TSTG | -25 ~ 100 | ℃ |
| Soldering Temperature | TSOL | 260 ℃ for 5 seconds |

*1. Keep the distance more than 2.0 mm from PCB to the bottom of LED package

▣ Electro-Optical Characteristics

(Ta=25℃)

| Parameter | Symbol | Condition | Min | Typ | Max | Unit |
| --- | --- | --- | --- | --- | --- | --- |
| Short Circuit Current | ISC | EV = 1000 lux |  | 57 |  | ㎂ |
| Dark Current | ID | VR = 10 v |  | 1 | 10 | nA |
| Open Circuit Voltage | VOC | EV = 1000 lux | 0.3 | 0.32 |  | V |
| Capacitance | CT | V=3V, f=1MHz |  | 30 | 50 | pF |
| Spectrum Sensitivity | λ | - | 750 |  | 1100 | nm |
| Peak Sensing Wavelength | λP | - | - | 940 | - | nm |
| Half Angle | △θ | - | - | ±60 | - | Deg. |

** Short/Open Circuit : PARALLED LIGHT OF 1000lux illumination was applied By tungsten lamp of 2856K

|  |  | Spec. No. | HP-L322 |
| --- | --- | --- | --- |
|  | SINGLE PHOTO DIODE:750~1100nm | Part | SENSOR |

5. ELECTRO-OPTICAL CHARACTERISTICS CURVES

| ` |  | Spec. No. | HP-L322 |
| --- | --- | --- | --- |
|  | SINGLE PHOTO DIODE:750~1100nm | Part | SENSOR |

6. SELECTION GUIDE : CLASSIFICATION BY NAME

# Text boxes

2007/2-Rev : 1.3

HPD-5040B

Electronics corp.

HANSE SENSOR SERIES

SPECIFICATION

HANSE ELECTRONICS CORP.

TEL : 82-31-206-2851   FAX : 82-31-206-2850

http://www.e-hanse.com

HESP-KA-034

1/6

2007/2-Rev : 1.3

HPD-5040B

Electronics corp.

HANSE SENSOR SERIES

HANSE ELECTRONICS CORP.

TEL : 82-31-206-2851   FAX : 82-31-206-2850

http://www.e-hanse.com

HESP-KA-034

2/2

2007/2-Rev : 1.3

HPD-5040B

Electronics corp.

HANSE SENSOR SERIES

(Unit : mm)

2-□0.5

5.0

HANSE ELECTRONICS CORP.

TEL : 82-31-206-2851   FAX : 82-31-206-2850

http://www.e-hanse.com

HESP-KA-034

3/6

2007/2-Rev :1.3

HPD-5040B

Electronics corp.

HANSE SENSOR SERIES

HANSE ELECTRONICS CORP.

TEL : 82-31-206-2851   FAX : 82-31-206-2850

http://www.e-hanse.com

HESP-KA-034

4/6

2007/2-Rev :1.3

HPD-5040B

Electronics corp.

HANSE SENSOR SERIES

■ Radiation Characteristics

■ Relative Radiant intensity vs. Wavelength  : PEAK SENSING  : 940nm

HANSE ELECTRONICS CORP.

TEL : 82-31-206-2851   FAX : 82-31-206-2850

http://www.e-hanse.com

HESP-KA-034

5/6

2007/2-Rev :1.3

HPD-5040B

Electronics corp.

HANSE SENSOR SERIES

SENSOR CATEGORY

LS : LED FOR SENSOR  /  PD : PHOTO DIODE  /  PT : PHOTO TRANSISTOR

CHIP CHARACTERISTICS

A. LED FOR SENSOR- PEAK WAVELENGTH

850, 875 : Infra Red Emission – High Speed application

940 : Infra Red Emission

390, 400 : Ultra Violet Emission

570, 660 : Data Communication application

B. PD/PTR -CHIP CHARACTERISTICS- refer to data sheet

ENCAPSULATION TYPE

LENS SHAPE

L : Round type / F : Flat type / X : Axial type

PACKAGE SHAPE

- refer to package dimension sheet

HANSE ELECTRONICS CORP.

TEL : 82-31-206-2851   FAX : 82-31-206-2850

http://www.e-hanse.com

HESP-KA-034

6/6