| CUSTOMER : |  |
| --- | --- |
| DEVICE NAME : |  |
| MODEL NO. : |  |
| ISSUED DATE : |  |

[ CUSTOMER APPROVAL ]

| APPROVAL NO. |  |
| --- | --- |
| APPROVAL DATE |  |
| APPROVAL | INSPECTER | CHECK | APPROVAL | COMMENT |

[ SUPPLIER ]

| ISSUED DEPT. | ISSUE | REVIEW | REVIEW | APPR’D |
| --- | --- | --- | --- | --- |

- CONTENTS -

1. OVERVIEW

2. SPECIFICATION

3. ELECTRICAL CHARACTERISTICS

4. OPTICAL CHARCTERISTIC

5. INPUT LEVEL

6. FUNCTION

7. BLOCK DIAGRAM

8. TIMING CHART

9. PIN CONNECTION

10. DIMENSION

11. CONNECTION & CABLESTANDARD

12. THE RATE OF LIGHT TO TEMP CURVE

13. DATA SHIFT DIRECTION

14. EXAMPLE CONNECTION

15. MATTER ON CAUTION WHEN INSTALLED(assembly)

16. MATTER OF REFERENCE WHEN HANDLEING

# 1. OVERVIEW

16*32 LED dot matrix module to display.

It is integrated with SMD LED. This module is compact, slim and light.

It is suitable for the wide applications of a graphic & video board beyond a simple message board.

# 2. SPECIFICATION

| ITEM | DISCRIPTION |
| --- | --- |
| Size(WxHxD) | 160(W) x 80(H) x 9.2(mm) |
| Display Color | RED. GREEN. BLACK |
| Number of Dots | 512DOTS ( 32(W)x16(H)) |
| Drive mode | Dynamic Drive(1/16 duty) |
| Brightness Control | Controlled VR2 |
| View Angle | Horizontal: ±60° Vertical: ±60° |
| Weight | 50(±5g) |

# 3. ELECTRICAL SPECIFICATION

- Absolute Maximum Ratings(Ta=25°C)

| ITEM | SYMBOL | CONDITION | UNIT |
| --- | --- | --- | --- |
| DC Supply Voltage | Circuit | Vcc | 5 | V |
|  | LED | Vled | 5 | V |
| Input Voltage | Circuit | Vcc | Vcc(±0.3) | V |
|  | LED | Vled | Vled(-0.3) | V |
| Current Consumtion | Circuit | IC | 0.1(Vcc=5V) | A |
|  | LED | IL | 1.2(Vled=5V) | A |
| Clock Frequency | F | 25 | MHz |
| Operating Temperature | Topr | -20 ~ +65 | ℃ |
| Storage Temperature | Tstg | -20 ~ +85 | ℃ |
| Isolation Temperature | Viso | AC500V(10mA), 1Minute(connector~supporter) |

- RECOMADABLE DRIVE CONDITIONS

| ITEM | SYMBOL | CONDITION | UNIT |
| --- | --- | --- | --- |
| DC Supply Voltage | Circuit | Vcc | 5 | V |
|  | LED | Vled | 5 | V |
| Operating Temperature | Topr | -20 ~ +45 | ℃ |

# 4. OPTICAL CHARCTERISTIC

| ITEM | SYMBOL | MIN. | TYP. | MAX. | UNIT |
| --- | --- | --- | --- | --- | --- |
| Luminous intensity | RED GREEN | Lv | - | 700 500 | - | cd/㎡ |
| Peak Emisson Wave length | RED GREEN | Λp | - | 630 570 | - | nm |

# 5. INPUT LEVEL

| ITEM | SYMBOL | MIN. | TYP. | MAX. | UNIT |
| --- | --- | --- | --- | --- | --- |
| Input “L” | ViL | - | - | 0.8 | V |
| Input “H” | ViH | 2.4 | - | - |  |

# 6. FUNCTION

| ITEM | PIN NAME | DESCRIPTION | PIN No. |
| --- | --- | --- | --- |
| Power Pin | VCC | Power supply for the circuit | 1 |
|  | GND | Groung of the module | 2,3 |
|  | VLED | Power supply for the LED | 4 |
| Data Pin | green Data(GD) | Data input for green color | 6 |
|  | Red Data(RD) | Data input for red color | 8 |
|  | Line Address(A0~A3) | Signal input for line address | 9,10,11,12 |
|  | Clock(CLK) | Clock signal for data input and display | 4 |
|  | Latch(LA) | Signal input for data latch (New data latch at rising edge) | 2 |
|  | Out Enable(OE) | Display ON or OFF control (“H” display off, “L” display on) | 1 |
|  | GND | Groung of the module | 3,5,7 |

# 7. BLOCK DIAGRAM

# 8. TIMING CHART

- OPERATING TIMING

| UNIT | MAX. | MIN. | SYMBOL | CHARACTORISTICS |
| --- | --- | --- | --- | --- |
| MHz | 25 | - | T | Clock Cycle |
| ns | - | 5 | Tsu | Data Setup Time |
| ns | - | 20 | Th | Data Hold Time |
| ns | - | 20 | Tpw | Latch Pulse Width |
| ns | - | 20 | Tckl | Clock Latch Time |
| ns | - | 200 | Tepw | Enable Pulse Width |
| us | - | 1.5 | Tae | Address Enable Time |
| us | - | 1.5 | Tla | Latch Address Time |

# 9. PIN CONNECTION

- DATA SIGNAL FUNCTION(J1, J2)

| DESCRIPTION | PIN | CONNECTOR |
| --- | --- | --- |
|  | NAME | NUM. |  |
| Out Enable | OE | 1 |  |
| Data strobe | LA | 2 |  |
| Ground of the module | GND | 3 |  |
| Clock signal for input data | CLK | 4 |  |
| Ground of the module | GND | 5 |  |
| Data Input for ROW0 ~ ROW15 green color | GD | 6 |  |
| Ground of the module | GND | 7 |  |
| Data Input for ROW0 ~ ROW15 red color | RD | 8 |  |
| Data address 0 | A0 | 9 |  |
| Data address 1 | A1 | 10 |  |
| Data address 2 | A2 | 11 |  |
| Data address 3 | A3 | 12 |  |

# 10. DIMENSION

# 11. CONNECTION & CABLESTANDARD

- J1,J2 FFC Cable

- J3 Power Cable

| SPEC. | MODEL NO. | CONNECTION N0. |
| --- | --- | --- |
| 12P*50*1.00(0.1*0.75) | FFC12P 1.0mm | J1, J2 |
| J3 to P1,P3 : 300mm J3 to P2 : 150mm | GH-0322-300R | J3 |

3) J3 Power

# 12. THE RATE OF LIST DERATING CURVE

# 13. DATA SHIFT DIRECTION

# 14. EXAMPLE CONNECTION

# 15. MATTER ON CAUTION WHEN INSTALLED (assembly)

- It should be installed deeply considered in noisy place because wrong operation might be occurred

- Make sure of power source before operating after being assembled module. Damage may be occurred by low voltage or short circuit.

- The module is not waterproofed. So, do waterproof treatment to instrument of you need.

- Please install module within guaranteed scope and specially escape installation from circumstance of smoke, dust, and SO2-GAS.

- Please tern off power source if there is no data transmission when you testing its operation after installation.

- Please establish policy of heat release and use it under circumstance within guarantee scope in case a lot of module is assembled and used.

- In case it is used under below zero circumstance, it is favolable to use it with high voltage within maximum extent of value of input power source.

- Please make instrument after examining weight fully as module weight if 80g.

# 16. MATTER OF REFERENCE WHEN HANDING

- Over voltage prevention circuit is built in “LED POWER SUPPLY(VLED)” of module and LED will be turned off in casehigh voltage so supplied beyond maximum extent of regular power.

- VR volume of brightness adjustment-use id adjusted in fixed rank by LOT and supplied therefore don’t operate it as you please.

- Operating circuit is composed of CMOS, so, please take caution for static electricity.

- If you have any question for using this, please contact us.

※ Warranty contents

Exchange without compensation will be made for the period of 12month after having been delivered in case troubles in ordinary treatment in occurred.

Warranty is for deliver products. Expense of exchange work, damage compensation for advertisement suspension is not paid. Also compensative treatment will be made in case of following even for warranty period.

- Troubles by handing carelessness and wrong using.

- Troubles by inapplicable repair or remarking.

- Troubles by natural disaster.

◎ Matters that demand attention and notice in compliance with contents of this document and use of the product.

- In case that the products mentioned in this document is application ti foreign exchange and foreign control law, admission of Korea government is required when exporting or taking out.

- Technical information mentioned in this document is record of production characteristics and practical circuit and it is not mean guarantee of possessive right of industry or permission if performance right.

- Standard use of this production – it is used for general electronic parts(dedicators, Display, Office machine measuring equipment and home consumer products). When it is used for specific use(Aviation space, Traffic equipment. Burning equipment and safety equipment, ETC) which special quality and reliability is required and when trouble or miss operation of these threaten human’s life of do harm to person, you should discuss it whit us in advance considering using except standard use of our intention.

- You should use it within the warranty scope for special maximum rating operation power source electronic voltage scope and heat release ability. We are not responsible for the defect that occur to instrument when it is used beyond our warranty measures.

◎ If you have any question or change required about the specification, please solve it after agreement with us.

# Text boxes

SPECIFICATION

2-□0.5

5.0